## Slide 1: ITU 08215: MOBILE COMPUTING
LEARNING UNIT-1

## Slide 2: Learning OUTCOMES
After completing this course you should be able to:
  Explain what mobile computing is and give real examples.
  Compare types of mobility (macro, micro, ad‑hoc) and the protocols that support them.
  Analyze mobile hardware constraints.
  Differentiate between connectivity technologies.
  Apply frequency reuse formulas to calculate channel capacity.
  Describe how fading, interference, and handover affect communication.
  Recognize key software, UI, and security considerations for mobile apps

## Slide 3: REFERENCE
B’Far R (2005) Mobile Computing Principles : Designing and developing Applications with UML and XML. Cambridge University Press
Wigley, A., Moth, D. and Foot, P. (2010) Microsoft Mobile Development Handbook. Microsoft Press
Burnette, Ed. (2010). Hello, Android: introducing Google’s mobile development platform. 3rd ed. Raleigh, N.C.: Pragmatic Bookshelf.

## Slide 4: INTRODUCTION
From the early days of cellular communication to the advent of powerful smartphones and tablets, mobile computing has become an integral part of our daily lives, enabling us to access information and services anytime, anywhere.
Mobile computing is a technology that allows transmission of information (data, audio, and video) via computing devices that are not connected with any physical link (wirelessly).

## Slide 5: INTRODUCTION
The key features of mobile computing are: the computing devices are portable, Mobile and connected over a network.
The major elements of mobile computing are mobile communication, mobile hardware, and mobile software.
Goal of Mobile Computing: “People and their machines should be able to access information and communicate with each other easily and securely, in any medium or combination of media – voice, data, image, video, or multimedia – anytime, anywhere, in a timely, cost-effective way.”
Notes: Mobile computing vs Stationary computing

## Slide 6: BLOCK DIAGRAM OF WIRELESS COMMUNICATION

## Slide 7: TYPES OF MOBILITY
Macro-mobility: This is mobility through a global network. While moving in such a network, it should be possible to communicate without breaking the existing access. mobile IP, which is the protocol that takes care of macro-mobility.
Micro-mobility: This is mobility of a device in one single administrative domain of the global network. For cellular networks, this is the lowest level of mobility. Cellular IP is the protocol designed to take care of micro-mobility.

## Slide 8: TYPES OF MOBILITY
Ad hoc mobility: This is mobility within a mobile ad hoc network (MANET), caused by device mobility constantly changing the network topology.
Notes: User mobility, service mobility and Device mobility

## Slide 9: WHY IS MOBILITY IMPORTANT IN MOBILE COMPUTING
User convenience and flexibility
Support for remote work and field operations
Continuous access to services
Enhanced productivity and responsiveness
Notes: User mobility, service mobility and Device mobility

## Slide 10: MOBILE COMPUTING LIMITATIONS
Range & Bandwidth: Mobile Internet access is generally slower than direct cable connections,
Security standards: When working mobile, one is dependent on public networks.
Power consumption: rely entirely on battery power
Transmission interferences: Weather, terrain, and the range from the nearest signal point can all interfere with signal reception.
Potential health hazards: more likely to be involved in traffic accidents.
Human interface with device: Screens and keyboards tend to be small, which may make them hard to use.

## Slide 11: MOBILE HARDWARE COMPONENTS
Mobile computing devices have almost the same components as a normal computer but may be different in size to make it portable.
The following are some of the main mobile computing components:-
  CPU, Memory, Display, Battery, Connectivity, and Sensor

## Slide 12: CENTRAL PROCESSING UNIT
The CPU (Central Processing Unit) is the brain of any mobile computing device, responsible for executing instructions, running applications, and managing system performance.

## Slide 13: TYPES OF CENTRAL PROCESSING UNITs
Mobile CPUs can be categorized into two:
Architecture base (ARM, X86)
Core base (Single, Multi and Big.Little)

## Slide 14: DESIGN CONSTRAINTS OF MOBILE CPUs
Power Consumption: Mobile CPUs must balance performance and battery life
Heat Dissipation: Unlike desktop CPUs, mobile CPUs do not have cooling fans
Size & Integration: Mobile CPUs must be compact to fit within thin devices
Performance vs. Efficiency Trade-off: High performance consumes more power and generates more heat

## Slide 15: BATTERY
Battery — the limited battery capacity of mobile devices can restrict their usage time and can often be a source of frustration for users.
Some of the reasons that cause battery constraints in mobile computing are: Small size and weight, mobile features such as GPS, camera and internet connectivity, battery degradation.
List the technologies that have been developed to improve battery life.

## Slide 16: EXAMPLE
To illustrate the constraint of limited available power, consider a laptop computer with a CD-ROM and a display. The constant power dissipation in a CD-ROM (for disk spinning) is approximately 1.0 W and the power dissipation for the display is approximately 2.5 W. Assume a cell used as power source is rated to give 800 mA-Hr at 1.2 V (0.96 W-Hr). How long does the assumed power source last?
What do you think can be done to increase the longevity of the cell chosen?

## Slide 17: General Battery key design constraints
Energy density
Safety
Cycle life
Temperature sensitivity
Fast charging
Environmental impact

## Slide 18: screen
Touch screen — is an input device that allow users to give a desire command by simply touching the display screen. A touch screen kit includes the following components:-
  Touch sensor: Clear glass panel with responsive surface
  Controller: Card that connects the touch sensor and the device.
  Driver
There are two primary themes to consider when it comes to smartphone touchscreens:-
  Sensitivity
  Resolution quality

## Slide 19: TYPES OF Touchscreen
There are couple of different touchscreen nowadays that includes:-
  Resistive screen
  Capacitive touch screen
  Haptic screen
  AMOLED (Active Matrix Organic Light Emitting Diode) screen

## Slide 20
Form a group and choose one mobile computing hardware component to explain its functionality, types and design constraints

## Slide 21: CONNECTIVITY IN MOBILE DEVICES
There are so many ways of adapting connectivity in mobile devices such as:
  Cellular networks is a system of wireless communication that uses radio waves to connect mobile devices to each other and the internet.
  Wi-Fi is a popular connectivity solution for mobile devices. Wi-Fi provides faster speeds and can be more cost-effective than cellular networks.
  Near Field Communication (NFC) is a wireless communication technology that enables mobile devices to interact with other devices and objects that are equipped with NFC technology. This technology is commonly used for contactless payments and data transfers.

## Slide 22: BASICs of NFC
  Near Field Communication (NFC) is a set of short-range wireless technologies, typically requiring a distance of 4 cm or less to initiate a connection.
  NFC lets you share small payloads of data between an NFC tag and an Android-powered device, or between two Android-powered devices.
  For more information about NFC visit: https://developer.android.com/develop/connectivity/nfc/nfc

## Slide 23: BASICs of NFC
  Android-powered devices with NFC simultaneously support two main modes of operation:
    Reader/writer mode, allowing the NFC device to read and write passive NFC tags and stickers.
    Card emulation mode, allowing the NFC device itself to act as an NFC card. The emulated NFC card can then be accessed by an external NFC reader, such as an NFC point-of-sale terminal.

## Slide 24: CONNECTIVITY IN MOBILE DEVICES
Bluetooth is a short-range wireless connectivity technology that is commonly used to connect mobile devices to other devices, such as wireless headphones, speakers, and car audio systems over a short distance typically up to 10 meters.
  ZigBee is a wireless technology specifically developed to replace Bluetooth and Wi-Fi. It commonly used in home automation applications such as: Lighting control, temperature control and security systems.

## Slide 25: Generation of cellular networks
1G: Analog voice services (AMTS)
2G: Digital voice and basic data (GSM, CDMA,TDMA)
3G: Enhanced data services (UMTS, HSPA)
4G: High-speed data and IP-based services (LTE)
5G: Ultra-low latency, massive connectivity, enhanced broadband

## Slide 26: ADVANCED MOBILE PHONE SYSTEM
Used in North America
Uses 800MHz ISM band (Industrial Scientific Medical purpose)
From BS to MS: Forward communication---869 to 894 MHz: downlink of 25MHz
From MS to BS: Reverse communication---824 to 849 MHz: uplink of 25MHz
Channel spacing is 30 KHz, Total # of channels is 832
Location area is shared by two service provider with 416 channels
12 are control channels and 395 are voice channels

## Slide 27: Cellular digital packet data
Designed to provide packet data services on top of AMPS without interfering with voice calls.
Data transmission prioritizes voice calls; data can only use channels not occupied by voice calls.

## Slide 28: Limitations of G
Low capacity
Poor voice quality
Poor battery life
Large phone size
No security

## Slide 29: G: Architecture of GSM Network

## Slide 30: Function of GSM components
Base Station Sub-system
  Handles traffic b/w MS and NSS
  Two main components: Base Transceiver Station (handle communication to ME) and Base Station Controller (Allocate time slots b/w BTS and ME)
  Network Support Sub-system
    It tracks the location of callers to enable cellular services
    Five main components:
      Mobile Switching Center (Performs call setup, call release, call tracing, call forward and short message services)

## Slide 31: Function of GSM components
  Network Support Sub-system
    Home Location Register( Subscriber's ID, Plan, Caller tune, Location authentication using SIM cards)
    Visitor Location Register( Exact location of all subscribers current present in service area of MSC)
    Equipment Identification Register(Database with records of allowed and banned ME)
    Authentication Center( Authenticate user in the network)

## Slide 32: G: Architecture Network (UMTS)

## Slide 33: G: Architecture Network (UMTS)

## Slide 34
Explain the features of radio communication that are important from a standpoint of software development

## Slide 35: BANDWIDTH SHARING AND CHANNEL RE-USE
Bandwidth in radio-based networks is shared among users, leading to more severe limitations compared to wired networks.
However, channels (frequency or time slots) can be reused if physically distant enough, enabling efficient utilization of available spectrum.
This concept underlies the architecture of wireless systems, which are divided into physical cells that can reuse channels.
Cellular network is organized into multiple low power transmitters each 100w or less
Notes: Reuse factor, reuse pattern and reuse distance

## Slide 36: BANDWIDTH SHARING AND CHANNEL RE-USE
Notes: Reuse factor, reuse pattern and reuse distance

## Slide 37: CHANNEL RE-USE TECHNICAL TERMS
Cluster size (N)
A cluster is the minimum group of cells that collectively use the entire available frequency spectrum without adjacent cells sharing the same frequencies. It is calculated using the shift parameters and .
Common values for (N) in GSM are 3, 4, 7, 9, 12, or 13.
Notes: Reuse factor, reuse pattern and reuse distance

## Slide 38: CHANNEL RE-USE TECHNICAL TERMS
Frequency reuse factor (N)
This indicates how many times a specific frequency channel can be reused across the network. It is the reciprocal of the cluster size:
Notes: Reuse factor, reuse pattern and reuse distance

## Slide 39: CHANNEL RE-USE TECHNICAL TERMS
Co-channel reuse distance (D)
This is the minimum physical distance that must separate two cells using the exact same frequencies to avoid co-channel interference. It depends on the cell radius (R) and cluster size (N)
Notes: Reuse factor, reuse pattern and reuse distance

## Slide 40: CHANNEL RE-USE TECHNICAL TERMS
System capacity calculation
To find out how many simultaneous channels the entire network can support, use the formula:
Where M:Number of times the cluster is repeated across the total coverage area
N:Cluster size
k: Number of channels allocated to each individual cell
Notes: Reuse factor, reuse pattern and reuse distance

## Slide 41: BANDWIDTH SHARING AND CHANNEL RE-USE
For example, when N cells are using the same number of frequencies and K be the total number of frequencies used in systems. Then each cell frequency is calculated by using the formula K/N.
In Advanced Mobile Phone Services (AMPS) when K = 395 and N = 7, then frequencies per cell on an average will be 395/7 = 56. Here, cell frequency is 56.

## Slide 42: examples
Draw frequency reuse pattern for cluster size N=4
A spectrum of 30MHz is allocated to wireless FDD cellular system which uses two 25 kHz simplex channels to provide full duplex voice and control channel. Compute number of channels available per cell if the system used 4 cell reuse pattern. Assume MHz spectrum is allowed to control channel. Give the distribution of voice and control channels.
A cellular system has 33 cells, system reuse factor is 4 and radius of each cell is 2 Km. The system is designed to support 343 traffic channel calculate: No of channel per cell, Geographical area covered and No of simultaneous call supported by system

## Slide 43: PROPAGATION MECHANISM
Wireless transmissions propagate in three modes:
Ground-wave propagation: follows the contour of the earth
Sky-wave propagation: uses reflection by both earth and ionosphere
Line-of-sight propagation: requires the transmitting and receiving antennas to be within the line of sight of each other. Depending upon the frequency of the underlying signal, the particular mode of propagation is followed

## Slide 44: Handover and cell switching
Handover is the process of transferring a call or data session from one cell to another as a user moves.
For example, imagine you're on a call while walking down the street. As you move out of one cell's coverage area, your device automatically switches to a neighboring cell without dropping the call.
This seamless transition between cells is essential for maintaining uninterrupted communication during mobility.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 45: Types of Handover and cell switching
Hard Handover: "Break before make" - connection to the original cell is broken before connecting to the new cell
Soft Handover: "Make before break" - device connects to the new cell before disconnecting from the original cell
Seamless Handover: Transition without noticeable interruption to service
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 46: Handover decision factor
Signal strength measurements
Signal quality (signal-to-noise ratio)
Distance from base station
Network load balancing
User velocity and direction
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 47: Software architecture for mobility
Mobility in cellular networks requires sophisticated software systems to manage handovers and ensure seamless connectivity.
These software systems must track the movement of users, predict handover events, and coordinate communication between cells.
Think of the software as a traffic controller that directs data traffic and manages the handover process to optimize network performance and user experience.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 48: Software architecture for mobility
Mobility introduces challenges such as signal strength variations, handover delays, and network congestion.
To address these challenges, cellular networks deploy advanced technologies like adaptive antenna systems, handover optimization algorithms, and load balancing techniques.
These technologies help enhance network reliability, minimize dropped calls, and improve overall quality of service for mobile users
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 49: FADING
Fading is a common phenomenon in radio communication where the strength of a received signal fluctuates over time and space.
It occurs due to various factors such as multipath propagation, atmospheric conditions, and obstacles in the signal path.
Fading can lead to signal attenuation, distortion, and intermittent loss of connectivity, posing challenges for wireless communication systems.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 50: FADING
Short-term fading occurs when the transmitted signal takes multiple paths to reach the receiver, resulting in signal components arriving at different times and phases.
This phenomenon causes signal amplitude variations, leading to rapid fluctuations in signal strength.
Short-term fading is commonly observed in urban environments with buildings and structures causing signal reflections and scattering.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 51: FADING
Long-term fading occurs due to the topography of the terrain and large-scale obstacles such as mountains, hills, and buildings.
These obstacles create shadow regions where the signal is significantly attenuated or blocked entirely, leading to signal dropouts.
Long-term fading effects are more pronounced over longer distances and can persist for extended periods, affecting overall network coverage.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 52: Interference
Interference occurs when unwanted signals from other sources disrupt the communication between a transmitter and receiver.
Interference can arise from various sources, including neighboring cells, adjacent channels, electronic devices, and environmental noise.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 53: Impact of Interference
Interference degrades the signal-to-noise ratio (SNR), increasing the likelihood of errors and reducing communication quality.
High levels of interference can lead to dropped calls, decreased data throughput, and degraded network performance.
Interference can be particularly problematic in densely populated areas or environments with high levels of electromagnetic noise.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 54: Mitigation technique for Interference
Frequency Planning
Frequency planning involves allocating different frequency bands to minimize interference between adjacent cells and channels.
By carefully selecting and coordinating frequencies, network operators can reduce co-channel and adjacent-channel interference.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 55: Mitigation technique for Interference
Interference Rejection Techniques
Advanced signal processing techniques such as adaptive filtering, interference cancellation, and spectrum sensing can help identify and mitigate interference.
These techniques enable receivers to suppress unwanted signals and improve the quality of desired signals.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 56: BIT ERROR RATE
Bit Error Rate (BER) is a measure of the accuracy of data transmission in a communication system, indicating the probability of erroneous bits in the received data compared to the transmitted data.
BER is influenced by various factors such as signal-to-noise ratio (SNR), channel conditions, interference, and modulation scheme.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 57: Transmission power management
Transmission power management involves controlling the power levels at which signals are transmitted by devices in a communication system.
It plays a crucial role in optimizing signal quality, minimizing interference, conserving energy, and enhancing the overall performance of wireless networks.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 58: Factors that influence Transmission power management
Energy is a scarce resource in mobile units. Therefore, transmission with power as low as feasible is highly desirable.
Signals from other terminals are considered by a given terminal as interference, which has a negative effect on the signal-to-noise ratio. Thus, it is important that each terminal use the "right" amount of power to transmit successfully without unnecessary degradation of others' transmissions.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 59: example
Let us review the basic relationships among power, distance and signal-to-noise ratio. In the ideal free space, signal strength diminishes with the inverse square of the distance. For example, if the received signal is 100 watts at a distance of 1 mile, it will be 25 watts at 2 miles, 4 watts at 5 miles and 1 watt at 10 miles.
In practice, since mobile terminals do not move in free space but rather have to deal with various obstacles, the loss of power is much more significant, ranging from inverse cube of distance to exponents as high as the 6th power.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 60: Parameter at the application level
The wireless network your phone connects to has conditions, similar to road conditions during a trip. These conditions impact app performance.
Apps can adapt to these conditions, just like adjusting travel plans based on road conditions.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 61: Parameter at the application level
BER (Bit Error Rate) and SNR (Signal-to-Noise Ratio) are crucial
  BER: Measures data errors
  SNR: Measures signal strength.
Apps use this info to make smart decisions, like delaying data transfer during weak signal moments.
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 62: Parameter at the application level
Location and network cost are important
  Location: Crucial for maps and location-based services.
  Cost: Varies based on time and location; apps can adjust behavior to save money.
Adaptive Connectivity
  Phones can connect via different methods (cellular, Wi-Fi).
  Apps choose the best option based on circumstances
Notes: Soft handover is particularly useful in environments with rapidly changing signal conditions, such as urban areas with tall buildings or areas with high mobility.

## Slide 63: MOBILE SOFTWARE
Mobile applications/software have become essential in our daily lives, providing us with convenient access to various services and functionalities.
To develop mobile apps, developers often utilize frameworks tailored to specific mobile platforms.
There are various mobile app development frameworks available in the tech world that you can consider learning to build your own mobile application.

## Slide 64: MOBILE APP DEVELOPMENT FRAMEWORK
Mobile App Development Framework is a library that offers the required fundamental structure to create mobile applications for a specific environment.
In short, it acts as a layout to support mobile app development. Moreover, mobile application frameworks can be classified majorly into 3 categories:
  Native Apps: designed for a particular platform or device
  Web Apps: designed to deliver web pages
  Hybrid Apps:

## Slide 65: USER INTERFACE DESIGN
A user interface (UI) is the point of human-computer interaction and communication in a device.
It encompasses both hardware components (physical buttons, touchscreens, keyboards) and software components (menus, icons, buttons, forms).
UI exists across various processes and provides a means for users to input commands and receive output or feedback from the system.

## Slide 66: USER INTERFACE DESIGN
Traditionally, UI design focused primarily on output, with users interacting with character-based screens and command-line interfaces.
However, modern UI design has evolved into a two-way channel, with powerful output capabilities and user-driven customization options.
Today, successful applications are designed with a user-centered approach, prioritizing user needs and preferences.

## Slide 67: FOUR MAIN ELEMENTS OF UI DESIGN
Usability
  How easily and efficiently users can accomplish their goals using the interface.
    Example: Google's search interface with a simple search box and clear "Google Search" button
    Counter-example: Cluttered websites with too many options that overwhelm users

## Slide 68: FOUR MAIN ELEMENTS OF UI DESIGN
Visualization
  The visual representation of information and interface elements.
    Example: Apple's clean, minimalist design with plenty of white space and consistent iconography

## Slide 69: FOUR MAIN ELEMENTS OF UI DESIGN
Functionality
  How well the interface performs its intended tasks and meets user needs.
    Example: Netflix's recommendation system that suggests relevant content based on viewing history

## Slide 70: FOUR MAIN ELEMENTS OF UI DESIGN
Accessibility
  Ensuring the interface can be used by people with diverse abilities and disabilities.
    Example: Screen reader compatibility for visually impaired users
    Example: High contrast mode options for users with visual difficulties
    Example: Keyboard navigation alternatives for users who cannot use a mouse

## Slide 71: KEY DESIGN CONSIDERATION
Consistency
  Maintain uniformity across all interface elements including colors, borders, font sizes, styles, headers, footers, and background images.
Examples of Good Consistency:
  Bad Example: A website that uses different button styles on each page, confusing users about what's clickable
  Apple's iOS: Consistent use of rounded corners, specific blue color forlinks, and uniform spacing

## Slide 72: KEY DESIGN CONSIDERATION
Responsiveness
  Users expect immediate feedback when they interact with an interface. This includes both technical responsiveness (fast loading times) and interactive feedback (visual confirmation of actions).
Examples:
  Button States: Buttons that change color when hovered over or pressed
  Loading Indicators: Progress bars or spinners that show system activity
  Form Validation: Real-time feedback when users enter incorrect information

## Slide 73: KEY DESIGN CONSIDERATION
Familiar Language and Terminology
  Use words and terms that users already understand from their daily experience or previous interactions with similar systems.
Examples:
  Good: "Save" instead of "Persist Data"
  Good: "Shopping Cart" instead of "Item Repository"

## Slide 74: KEY DESIGN CONSIDERATION
Clear Navigation and Contact Information
  Every page should provide easy access to essential information and navigation options, including company contact details.
Examples:
  Sticky Navigation: Headers that remain visible while scrolling
  Breadcrumbs: Showing users where they are in the site hierarchy (Home > Products > Laptops > Dell XPS)

## Slide 75: SEVEN HABITS OF SUCCESSFUL INTERFACE DESIGN
Understand the Business - Designers should have a thorough understanding of business requirements and objectives.
Maximize Graphical Effectiveness
Think Like a User
Use Models and Prototypes - Develop models and prototypes to test and refine the interface design.

## Slide 76: SEVEN HABITS OF SUCCESSFUL INTERFACE DESIGN
Focus on Usability - Prioritize usability to ensure that the interface is intuitive and easy to navigate.
Invite Feedback - Seek feedback from users and stakeholders to identify areas for improvement.
Document Everything - Maintain thorough documentation of the design process, decisions, and revisions.

## Slide 77: MAXIMIZE GRAPHICAL EFFECTIVENESS
Utilize graphical elements effectively to enhance the visual appeal and usability of the interface.
A well-designed interface can help users learn a new system rapidly and be more productive.
Also, in a graphical environment, a user can display and work with multiple windows on a single screen and transfer data between programs.
If the interface supports data entry, it must follow the guidelines for data entry screen design.

## Slide 78: MAXIMIZE GRAPHICAL EFFECTIVENESS
A good data entry form design can be discussed in these four categories:
  Structure
  Text
  Technical design
  Data validation

## Slide 79: STRUCTURE
Consider the following when designing the overall structure of a form:
  Structure everything vertically
  Rely on one column
  Don’t split numbers
  Break up long forms

## Slide 80: TEXT
The way you present text and write copy on your forms can have a big impact on overall conversion rates. Here are some tips to follow:
  Clear and concise labels
  Use action words for buttons
  Use first-person
  Separate placeholder text and label text

## Slide 81: TECHNICAL DESIGN
Some of the most important technical aspects of form design are:
  Autofill
  Keyboards
  Predictive search

## Slide 82: TECHNICAL DESIGN
There are two important concepts to cover with data validation.
  Validate data inline
  Autocorrect format errors
For more tutorial about data entry form design visit: GUIDELINES FOR DESIGNING USER INTERFACE SOFTWARE : 1. Data Entry (hcibib.org)

## Slide 83: WIRELESS APPLICATION PROTOCOL
The Wireless Application Protocol (WAP) is an industry-wide specification designed for applications that operate over wireless networks, primarily targeting mobile devices.
WAP plays a crucial role in enabling mobile users to access internet-based services and applications, optimizing content delivery for devices with limited bandwidth and screen size.
For more information about WAP: https://ebooks.inflibnet.ac.in/itp12/chapter/wap-wireless-application-protocol/

## Slide 84: WAP STACK

## Slide 85: WWW LOGICAL MODEL

## Slide 86: WIRELESS APPLICATION ENVIRONMENT
Wireless Application Environment (WAE), the uppermost layer in the WAP stack, provides an environment that enables a wide range of applications to be used on the wireless devices.
It contains WML and WTA (Wireless Telephony Application). WAE includes a micro-browser server environment which provides:
  WML
  WML script
  WTA
  Content formats

## Slide 87: WAE LOGICAL MODEL

## Slide 88: WIRELESS MARKUP LANGUAGE
WML is a markup language based on XML (eXtensible Markup Language), specifically designed for creating content and applications for wireless devices, particularly mobile phones.
Developed and maintained by the WAP Forum, WML serves as a standard for building mobile-friendly web pages and applications.

## Slide 89: SYNTAX AND STRUCTURE OF WML DOCUMENT
Prolog
The prolog is the first statement within a WML document and is optional. It includes two lines of code specifying the XML version and the document type definition (DTD) for WML, which ensures compliance with the WML specification.
Unit of Navigation
In HTML, the basic unit of navigation is a page, while in WML, it is a card. WML documents can contain multiple cards arranged in a deck.
Each card represents a separate screen or page of content.

## Slide 90: SYNTAX AND STRUCTURE OF WML DOCUMENT
Document Element
In WML, the document element is <wml>, and all other elements are contained within it. This element serves as the root of the WML document and encapsulates the entire content.
Elements and Attributes
WML documents consist of predefined elements, such as <card> and <p>, which are used to structure and present content.
Elements are denoted by opening and closing tags, while attributes describe the characteristics of elements.

## Slide 91: LIMITATION OF WIRELESS APPLICATION PROTOCOL
WTLS (Wireless Transport Layer Security) terminates at WAP gateway
Data is briefly unencrypted at the gateway before being re-encrypted with TLS/SSL
This creates a potential security vulnerability point
Operators control these gateways and can potentially access decrypted data

## Slide 92: SECURITY IN MOBILE COMPUTING
Mobile computing security presents unique challenges that differ significantly from traditional desktop or server security.
The fundamental issue stems from the distributed nature of mobile environments where multiple stakeholders control different components of the system, creating a complex security landscape that requires careful coordination and standardization.

## Slide 93: SECURITY IN MOBILE COMPUTING
In a mobile computing environment, the user can move from one network to another, one device to another or one bearer to another.
Therefore, theoretically the security implementations need to be device independent, network independent, bearer independent, and so on.
The requirement is to arrive at a security model, which can offer homogenous end-to-end security.

## Slide 94: SECURITY IN MOBILE COMPUTING
Real-World Example:
When you use a banking app on your phone, your transaction data travels through:
Your device → Cell tower → Mobile operator's network → Internet → Bank's servers
Each hop involves different security policies and potential vulnerabilities

## Slide 95: SECURITY IN MOBILE COMPUTING
Network mobility:
Scenario: User travels from Country A to Country B
Security Challenges:
Policy Inconsistencies: Each network may have different security requirements
Authentication Complexities: Roaming agreements may not include robust security protocols
Data Protection Variations: Different countries have different privacy laws
Billing Fraud: Roaming creates opportunities for billing-related security attacks

## Slide 96: SECURITY IN MOBILE COMPUTING
Bearer mobility:
Scenario: User move from 3G to 4G or Bluetooth
Each Bearer's Security Profile
  3G/4G: Carrier-controlled, standardized security protocols
  WiFi: Varies by access point, potentially unsecured
  Bluetooth: Short-range, device-specific security
Security Challenges:
Security policies must adapt in real-time as bearers change

## Slide 97: SECURITY IN MOBILE COMPUTING
Strong security controls must be implemented while creating mobile computing applications in order to guard against potential threats and weaknesses. Here are some crucial security precautions to take into account:
  Secure Coding Practices: Follow secure coding practices, such as avoiding hard-coded credentials, using secure libraries and frameworks, and properly handling errors, exceptions, and log in
  Secure Updates and Patch Management: Keep the mobile application up-to-date with the latest security patches and updates. Regularly monitor for security updates for the operating system, libraries, and components used in the application, and promptly apply patches to address known vulnerabilities.

## Slide 98: SECURITY IN MOBILE COMPUTING
  Secure Authentication and Authorization: Implement strong authentication and authorization mechanisms to ensure that only authorized users have access to the application and its resources.
  Data encryption: To encrypt data, both in transit and at rest, use powerful encryption algorithms. Data is protected by encryption from illegal access and interception, making sure that even if data is intercepted, it is difficult to decipher.

## Slide 99: THREAT MODELING
Threat modeling: is a proactive approach that involves identifying and mitigating potential threats and vulnerabilities in the mobile application during the development process.
The development team should take into account the mobile application's architecture, design, data flows, user interactions, external dependencies, and threat scenarios when doing threat modeling.
  Attacker’s perceptive
  Architectural perceptive
  Asset perceptive

## Slide 100: THREAT MODELING
For conducting threat modeling, there are various approaches and frameworks available, including:
  STRIDE (Spoofing, Tampering, Repudiation, Information Disclosure, Denial of Service, Elevation of Privilege),
  DREAD (Damage potential, Reproducibility, Exploitability, Affected users, Discoverability),
  OCTAVE (Operationally Critical Threat, Asset, and Vulnerability Evaluation).